## Slide 1: Python Scripting with Network
Day 10

## Slide 2: Agenda
Python Network Controllers
Python Classes
Python Packages
Python Netmiko Library
Python Nornir Library

## Slide 3: Python Network Controller API
A Python network controller is typically a Software-Defined Networking (SDN) framework or an automation engine written in Python that centralizes the management of network switches, routers, and firewalls.
It separates the control plane from the data plane, allowing engineers to programmatically dictate traffic, optimize routing, and manage devices.

## Slide 4: Python Classes
Classes are created using class keyword. Attributes are variables defined inside class and represent properties of the class. Attributes can be accessed using dot . operator (e.g., MyClass.my_attribute).
An object is a specific instance of a class. It holds its own set of data (instance variables) and can invoke methods defined by its class. Multiple objects can be created from same class, each with its own unique attributes.

## Slide 5: Python Packages
If you are working with physical hardware (switches, routers) or infrastructure, these packages streamline device communication, configuration, and testing.
Netmiko: A multi-vendor library built on Paramiko that simplifies SSH connections to network devices, allowing you to easily send CLI commands and retrieve outputs.
NAPALM: An abstraction layer that lets you interact with different networking vendors (Cisco, Juniper, Arista) using a single, uniform API.
Nornir: An automation framework written specifically for network engineers that allows you to run tasks concurrently against hundreds of devices.

## Slide 6: Python NetworkX library
NetworkX is a Python package for the creation, manipulation, and study of the structure, dynamics, and functions of complex networks. It provides:
tools for the study of the structure and dynamics of social, biological, and infrastructure networks;
a standard programming interface and graph implementation that is suitable for many applications;
a rapid development environment for collaborative, multidisciplinary projects;
support for algorithm acceleration and additional features through third-party backends;
an interface to existing numerical algorithms and code written in C, C++, and FORTRAN; and
the ability to painlessly work with large nonstandard data sets.
With NetworkX you can load and store networks in standard and nonstandard data formats, generate many types of random and classic networks, analyze network structure, build network models, design new network algorithms, draw networks, and much more.

## Slide 7: Python Netmiko Library
Successfully establish an SSH connection to the device.
Simplify the execution, retrieval, and formatting of show commands.
Simplify the execution of configuration commands.
Abstract away much of the low-level mechanics of interacting with devices.
Provide a (relatively) uniform API for interacting with devices.
Do the above across a broad set of networking vendors and platforms.

## Slide 8: Python Nornir Library
Nornir is an open-source, pluggable, multi-threaded automation framework written in Python and designed to be used directly with native Python code. Unlike traditional configuration management tools like Ansible, which rely on a Domain-Specific Language (DSL) or cumbersome YAML files, Nornir lets you orchestrate workflows using standard Python scripts.
Pure Python Execution: Write all your tasks, conditionals, loops, and logic natively in Python.
Built-in Concurrency: Features a multi-threaded task runner that operates rapidly across large device inventories.
Native Inventory Management: Organizes and accesses host data, variables, credentials, and custom metadata.

## Slide 9: Wrap Up
Python Automation for Network engineering
Python Network Libraries
Python Modules
Python Lambda Functions